## Slide 1: 基于通量重构方法的 高精度湍流模拟研究
博士研究生：朱辉
指导教师：符松 教授
2017.5

## Slide 2: 目录
绪论
通量重构方法
高精度隐式大涡模拟研究
前台阶转捩流动研究
结论与展望

## Slide 3: 1.绪论

## Slide 4: 从“LAST”谈起
Laboratory for Advanced Simulation of Turbulence
传统湍流模拟
  传统湍流模拟方法：RANS
  传统数值方法：二阶有限体积法/ 多块结构网格
先进湍流模拟
  精细湍流模拟方法：DES/ LES/ DNS
  新型数值方法：高分辨率格式/ 高精度方法/ 非结构网格

## Slide 5: 高精度数值方法
实现高精度的关键
  单元内多项式分布
  通量/守恒量积分点
一般原则：
  精度=多项式次数+1
  积分精度与求解精度匹配
多项式表达
  基函数+DOF
  Modal：正交多项式基，DOF物理意义不明确
  Nodal：Lagrange多项式基，DOF就是节点的值
李万爱，博士论文，《非结构网格高精度数值方法的若干问题研究》

## Slide 6: 高精度精细湍流模拟（1）
直接数值模拟（DNS）
  高精度有限差分
  Li. et. al. 高超声速边界层
  简单外形
  低雷诺数
大涡模拟
  Nagarajan 紧致有限差分
  Toro ADER
  壁面处理
Li XL, Fu DX, Ma YW. Direct numerical simulation of a spatially evolving supersonic turbulent boundary layer at Ma= 6
Nagarajan S, Lele S K, Ferziger J H. A robust high-order compact method for large eddy simulation Titarev V A, Toro E F. ADER schemes for three-dimensional non-linear hyperbolic systems.
Notes: 李新亮，高超声速DNS
Paul Tucker, 高阶LES

## Slide 7: 高精度精细湍流模拟（2）
雷诺平均（RANS）& 脱体涡模拟（DES）
  数值刚性
实现技巧
  “一维线搜索”
  自适应网格
  人工粘性/限制器
Gao J, Li X. Numerical Simulation of the Noise from Tandem Cylinder Flow with Spectral Difference Method
Shi L, Zhou C, Wang Z J. Adaptive RANS Solution with the High-order Correction Procedure via Reconstruction Method
Notes: 北航李晓东DES
周成2D SA

## Slide 8: 研究目标
基于高精度通量重构的大涡模拟
  隐式大涡模拟
基于高精度隐式大涡模拟的壁面模型
  如何克服数值刚性问题？
  如何避免对数区偏差？
高精度通量重构方法在流动转捩问题上的应用
  前台阶转捩流动

## Slide 9: 2.通量重构方法

## Slide 10: 通量重构方法（FR/CPR）
Flux Reconstruction
  也称为Correction Procedure via Reconstruction
Huynh 2007
节点型有限单元法 (Nodal FEM)
  单元内多自由度
  无显式数值积分
统一框架
  不同的修正系数对应了不同的高阶方法

## Slide 11: 通量重构方法（FR/CPR）
Solution Points & Flux Points
重构
  利用Solution Points上的值重构出多项式分布
单元界面：
  类似FVM，用Riemann Solver算连续通量
修正
  利用单元界面的连续通量修正多项式

## Slide 12: 数学形式
最终形式：在每个单元内
微分形式，避免了数值积分，比DG省计算量
每个单元仅受到相邻单元影响，数值格式是紧致的，边界条件实施较简单，容易并行化

## Slide 13: 粘性项的计算: BR2格式
简单处理 = “危险的”非物理解
  本单元梯度也需要修正过程，否则不守恒
  边界处梯度不能直接平均！(Cockburn & Shu 1998)
尽可能紧致！
Bassi-Rebay 2格式
  Bassi & Rebay (2000), for DG
  Huynh (2009): “翻译”到CPR框架下

## Slide 14: 曲边网格处理
直边网格
  网格稀疏
  法向量、面积等误差
曲边网格修正

## Slide 15: 计算程序MUSIC
多物理场模拟程序
  Multiphysics Simulation Code
  基于通量重构方法
  原始版本由ZJ Wang教授课题组开发
现代化程序
  采用C++编写，使用Petsc等第三方库
  预留多物理场求解接口
并行计算
  MPI，支持大规模并行（目前最多使用2000进程并行）
新型数值方法
  hp adaptation

## Slide 16: 测试算例
Theoretical Order | Grid Size | L2 Error | Actual Order
2 | 10*10 | 3.060e-2 | -
 | 20*20 | 7.295e-3 | 2.07
 | 40*40 | 1.933e-3 | 1.99
3 | 10*10 | 7.406e-3 | -
 | 20*20 | 1.032e-3 | 2.84
 | 40*40 | 1.385e-4 | 2.87
4 | 10*10 | 1.358e-3 | -
 | 20*20 | 1.028e-4 | 3.72
 | 40*40 | 7.330e-6 | 3.77

## Slide 17: 3.高精度隐式大涡模拟研究

## Slide 18: Large Eddy Simulation
基本思想&原理
  “过滤”
  解析大尺度，模化小尺度
  存在普适的频谱性质
  可能存在普适的模型
常见模型
  Static Smagorinsky
  Dynamic Smagorinsky
  Scale Similarity
  Mixing Model = Smagorinsky + Scale Similarity
  Implicit LES

## Slide 19: Smagorinsky模型的缺陷
基于混合长假设
  缺乏物理基础
纯耗散性
“可实现性”
壁面极限SGS应力不等于零
对于高阶格式，Implicit LES可能优于Smagorinsky
  Li and Wang 2015
隐式大涡模拟具有潜力
Li Y, Wang Z J. A priori and a posteriori evaluations of sub-grid scale models for the Burgers’ equation
Notes: 可实现性:亚格子k>0，实际上有更严格的要求

## Slide 20: 基于通量重构的隐式大涡模拟
以三阶通量重构方法为例（定性分析）
  由格式线性分析得出
  假设网格尺度处于惯性子区
  小于网格尺度时，等效粘性系数随波数增加升高
Domaradzki J A, Xiao Z, Smolarkiewicz P K. Effective eddy viscosities
in implicit large eddy simulations of turbulent flows

## Slide 21: Cylinder at ReD=3900 (1)
亚临界雷诺数
  层流边界层+湍流尾迹
P3曲边网格
  53,910单元数
  展向15层
三阶/四阶通量重构
隐式大涡模拟
初始条件：
  均匀场 + 非对称光滑扰动

## Slide 22: Cylinder at ReD=3900 (2)
壁面压力分布
  三阶、四阶均与实验符合良好

## Slide 23: Cylinder at ReD=3900 (3)

## Slide 24: Wall Modelled LES
降低壁面附近的网格量需求
三种常见策略
  改变边界条件：用切应力边界代替无滑移边界 (不稳定)
  嵌套网格：在壁面附近求解RANS方程 (复杂)
  涡粘模式：在壁面附近引入RANS涡粘系数 (✔）

## Slide 25: 新型壁面模型设计目标
不求解湍流模式方程
  数值刚性
远离壁面区域变为隐式大涡模拟
降低壁面附近流向&展向网格需求
  法向网格仍要求较密，以保持数值稳定
尽可能只使用“当地变量”
避免对数区不匹配

## Slide 26: S-A模式的近壁代数近似
Durbin 2004
粘性底层
  fv1分母趋于常数
  fv1整体正比于y+的三次方
  涡粘系数正比于y+的四次方
对数区
  fv1整体趋于1
  涡粘系数正比于y+

## Slide 27: Y+的计算
湍流边界层尺度定义
等应力层假设（零压梯度）
代入上述代数涡粘模式，积分此方程

## Slide 28: 新型壁面模型计算过程
在壁面第一层网格内
  取采样点计算
  目前取离壁面最远的求解点
根据u+和y+关系式求解y+
  Ridder’s算法，5到10步即可收敛
将y+插值到第一层网格内所有的求解点和通量点
  网格类型已知，求解点和通量点位置已知
  若对涡粘系数直接插值，易产生数值不稳定
判断最大y+
  若大于30，计算完成；否则在法向下一层网格中继续计算

## Slide 29: 槽道湍流(1)
三个不同雷诺数
  Reτ= 395, 640, 1140
不同网格
  流向、展向不同网格密度&法向网格分布
算例 | 名义Reτ | Nx×Ny×Nz | 第一层网格y+ | 第一个求解点y+ | 使用壁面模型
Case1 | 640 | 16×24×16 | 12 | 0.833 | 否
Case2 | 640 | 32×24×32 | 12 | 0.833 | 否
Case3 | 395 | 16×24×16 | 12 | 0.833 | 是
Case4 | 640 | 16×24×16 | 12 | 0.833 | 是
Case5 | 1140 | 16×24×16 | 12 | 0.833 | 是
Case6 | 640 | 16×24×16 | 8 | 0.556 | 是
Case7 | 640 | 32×24×32 | 12 | 0.833 | 是

## Slide 30: 槽道湍流(2)
如果不使用壁面模型：case 1, 2
  稀网格x+=50：速度型偏差，摩阻系数偏低20%
  加密到x+=25：稍有改善，但摩阻系数仍偏低10%

## Slide 31: 槽道湍流(3)
不同雷诺数：case 3,4,5
  Reτ=395, 640, 1140，
  均符合对数律分布
  截距5.0到5.5
网格敏感性验证：case4,6,7，Reτ=640
  法向网格分布：y+=8~12
  流向/展向加密
  基本上网格无关

## Slide 32: 槽道湍流(4)
壁面模型的转换区
  雷诺应力尖点对应于buffer layer速度拐折
  对其他区域几乎没有影响

## Slide 33: 周期山算例(1)
顺压/逆压梯度
  超出壁面模型设计范围
Reb = 2800, 10595
  低雷诺数：LES常见算例
  高雷诺数：ATAAC算例
网格：
  P3曲边网格
  Nx×Ny×Nz
  = 32×32×16
  高雷诺数下对应ATAAC稀网格

## Slide 34: 周期山算例(2)
无壁面模型
  再附点提前
有壁面模型
  再附点与参考值接近

## Slide 35: 周期山算例(3)
速度型

## Slide 36: 本章小结
基于通量重构的隐式大涡模拟
  亚网格等效粘性系数分析
  亚临界圆柱绕流算例
新型壁面模型
  近壁区：代数湍流模型
  远离壁面：隐式大涡模拟
  仅使用局部变量，适用于非结构网格

## Slide 37: 4.前台阶转捩流动研究

## Slide 38: 前台阶流动
二维几何扰动
  是否会引起转捩？
流动物理比后台阶更复杂
  两个分离区
基本参数
  台阶高度与边界层高度之比 （小于1）
  基于台阶高度的雷诺数 （处于转捩区间）
适用隐式大涡模拟
  显式LES难以计算转捩SGS应力
  DNS计算量难以承受

## Slide 39: 文献(1)
以雷诺数分类
  很低，关注小扰动的发展
    Wilhelm et. al. 2003 (JFM)：二维扰动如何变成三维扰动
  很高，关注湍流边界层
    Zukoski 1967 (AIAA J)：台阶前的第一分离区，超声速
    Sherry et. al. 2010：台阶后的第二分离区

## Slide 40: 文献(2)
转捩雷诺数
  Edelmann 2014 (DLR)
    台阶上游壁面吹吸与波包演化
    Reh = 400~4440
    扰动方程DNS
    线性稳定性分析
Edelmann C A. Influence of forward-facing steps on laminar-turbulent transition

## Slide 41: 问题与算例
台阶与入口扰动如何相互作用？（中等雷诺数）
Reh=720, Rexin=186624, Rexstep=330624
层流入口 + 有限扰动
  低频三维扰动，类似T-S波
四阶通量重构
DOF ≈ 1500万
展向宽度30h
展向32单元
统计50万时间步

## Slide 42: 平均流动(1)
速度型
与平板对比
  同样的入口扰动下，平板不转捩

## Slide 43: 平均流动(2)
湍动能
雷诺切应力
分离区

## Slide 44: 瞬时流动（1）
瞬时流向速度截面
  平板 vs 台阶

## Slide 45: 瞬时流动（2）
小尺度流向涡
  准定常
  Taylor-Gortler失稳

## Slide 46: 瞬时流动（3）
分离区
失稳、流向涡
K型转捩

## Slide 47: 频谱分析（1）
台阶上游
  St = 0.01主频
台阶面
  展向差别不大

## Slide 48: 频谱分析（2）
台阶下游
  依然以低频为主
  压力脉动幅度升高了一个量级

## Slide 49: 本章小结
采用高精度通量重构方法对前台阶诱导转捩流动进行了隐式大涡模拟
平板流动
  验证了入口扰动本身不能引起流动转捩
前台阶平均流动结果
  台阶前会产生流动分离，分离区外的流线会发生弯曲
前台阶瞬时流动结果
  Taylor-Gortler不稳定性，流向涡
  越过台阶面后，会在台阶下游边界层里诱导产生展向结构
  进一步发展形成发卡涡，K型转捩

## Slide 50: 5.总结与展望

## Slide 51: 总结
基于通量重构方法的隐式大涡模拟
  分析其数值性质
  圆柱绕流算例
适用于隐式大涡模拟的新型壁面模型
  代数形式
  仅使用当地变量
前台阶诱导转捩流动
  转捩机理

## Slide 52: 研究展望
基于高精度通量重构方法的隐式大涡模拟
  在高波数下会产生等效涡粘系数下降的现象
  可能与网格尺度过大时的计算不稳定性相关
  可能通过对通量重构方法进行修改从而获得更好的等效涡粘系数分布
新型壁面模型
  在转换区内仍存在速度拐折和雷诺应力偏差，通过调整过渡函数中的参数可能对这一现象得到改善
低速边界层中的前台阶诱导转捩流动
  不同雷诺数
  不同台阶高度

## Slide 53: 谢谢！

## Slide 54: 已发表的学术成果
[1] Hui Zhu, Song Fu, Lei Shi, and Z. J. Wang, "Implicit Large-Eddy Simulation for the High-Order Flux Reconstruction Method", AIAA Journal, Vol. 54, No. 9, (2016), pp. 2721-2733.
[2] Hui Zhu, Song Fu, "Forward Facing Step Roughness Effect on Hypersonic Boundary Layer Flow", APCOM 2014
[3] 朱辉，肖志祥，符松，某先进战斗机大攻角气动性能及其控制研究，国防技术报告, 2012
[4] Hui Zhu, Song Fu, Lei Shi, and Z. J. Wang, " A Hybrid RANS-Implicit LES Approach for the High-Order FR/CPR Method ", 54th AIAA Aerospace Sciences Meeting, 2016

## Slide 55: 参考文献（1）
Lax P D. Numerical solution of partial differential equations. The American Mathematical Monthly, 1965, 72(2):74-84.
Lax P D, Wendroff B. Difference schemes for hyperbolic equations with high order of accuracy. Communications on pure and applied mathematics, 1964, 17(3): 381-398.
Godunov S K, Zabrodin A V, Ivanov M I, Kraiko A N, Prokopov G P. Numerical solution of multidimensional problems of gas dynamics. Moscow Izdatel Nauka, 1976, 1.
Morinishi Y, Lund T S, Vasilyev O V, Moin P. Fully conservative higher order finite difference schemes for incompressible flow. Journal of computational physics, 1998, 143(1): 90-124.
Zhong X. High-order finite-difference schemes for numerical simulation of hypersonic boundary-layer transition. Journal of Computational Physics, 1998, 144(2): 662-709.
Li W, Ren Y X. High-order k-exact WENO finite volume schemes for solving gas dynamic Euler equations on unstructured grids. International Journal for Numerical Methods in Fluids, 2012, 70(6): 742-763.

## Slide 56: 参考文献（2）
Dumbser M, Käser M. Arbitrary high order non-oscillatory finite volume schemes on unstructured meshes for linear hyperbolic systems. Journal of Computational Physics, 2007, 221(2): 693-723.
Cockburn B, Shu C W. TVB Runge-Kutta local projection discontinuous Galerkin finite element method for conservation laws. II. General framework. Mathematics of Computation, 1989, 52(186): 411-435.
Huynh H T. A flux reconstruction approach to high-order schemes including discontinuous Galerkin methods // 18th AIAA Computational Fluid Dynamics Conference. 2007: 4079.
Hussaini M Y, Zang T A. Spectral methods in fluid dynamics. Annual review of fluid mechanics, 1987, 19(1): 339-367.
Karniadakis G, Sherwin S. Spectral/hp element methods for computational fluid dynamics. Oxford: Oxford University Press, 2013.
Wang Z J. Spectral (finite) volume method for conservation laws on unstructured grids. basic formulation: Basic formulation. Journal of Computational Physics, 2002, 178(1): 210-251.

## Slide 57: 参考文献（3）
Liu Y, Vinokur M, Wang Z J. Spectral difference method for unstructured grids I: basic formulation. Journal of Computational Physics, 2006, 216(2): 780-801.
Spalart P R. Detached-eddy simulation. Annual review of fluid mechanics, 2009, 41: 181-202.
Spalart P R, Deck S, Shur M L, Squires K D, Strlets M K, Travin A. A new version of detached-eddy simulation, resistant to ambiguous grid densities. Theoretical and computational fluid dynamics, 2006, 20(3): 181-195.
Travin A K, Shur M L, Spalart P R, Strelets M K. Improvement of delayed detached-eddy simulation for LES with wall modelling. // ECCOMAS CFD 2006: Proceedings of the European Conference on Computational Fluid Dynamics, Egmond aan Zee, The Netherlands, September 5-8, 2006. Delft University of Technology; European Community on Computational Methods in Applied Sciences (ECCOMAS), 2006.
Li X L, Fu D X, Ma Y W, Liang X. Direct numerical simulation of compressible turbulent flows. Acta Mechanica Sinica, 2010, 26(6): 795-806.
Xiao Z, Liu J, Huang J, Fu S. Numerical dissipation effects on massive separation around tandem cylinders[J]. AIAA journal, 2012, 50(5): 1119-1136.

## Slide 58: 参考文献（4）
Wang B, Zha G, Shen Y. Detached-Eddy Simulations of a Circular Cylinder Using a Low Diffusion E-CUSP and High-Order WENO Scheme //38th Fluid Dynamics Conference and Exhibit. 2008: 3855.
Nagarajan S, Lele S K, Ferziger J H. A robust high-order compact method for large eddy simulation. Journal of Computational Physics, 2003, 191(2): 392-419.
Titarev V A, Toro E F. ADER schemes for three-dimensional non-linear hyperbolic systems. Journal of Computational Physics, 2005, 204(2): 715-736.
Nguyen N, Persson P O, Peraire J. RANS solutions using high order discontinuous Galerkin methods //45th AIAA Aerospace Sciences Meeting and Exhibit. 2007: 914.
Gao J, Li X. Detached eddy simulation of flow over NACA0012 airfoil at high angle of attack with spectral difference method //52nd Aerospace Sciences Meeting. 2014: 0425.
Shi L, Zhou C, Wang Z J. Adaptive RANS Solution with the High-order Correction Procedure via Reconstruction Method //54th AIAA Aerospace Sciences Meeting. 2016: 1826.

## Slide 59: 参考文献（5）
Gao J, Li X. Numerical Simulation of the Noise from Tandem Cylinder Flow with Spectral Difference Method //54th AIAA Aerospace Sciences Meeting. 2016: 0256.
Ceze M, Fidkowski K. Pseudo-transient continuation, solution update methods, and CFL strategies for DG discretizations of the RANS-SA equations //21st AIAA Computational Fluid Dynamics Conference. 2013: 2686.
Oliver T, Darmofal D. An unsteady adaptation algorithm for discontinuous Galerkin discretizations of the RANS equations //18th AIAA Computational Fluid Dynamics Conference. 2007: 3940.
Bassi F, Crivellini A, Rebay S, Savini M. Discontinuous Galerkin solution of the Reynolds-averaged Navier–Stokes and k–ω turbulence model equations. Computers & Fluids, 2005, 34(4): 507-540.
Wang Z J, Gao H. A unifying lifting collocation penalty formulation including the discontinuous Galerkin, spectral volume/difference methods for conservation laws on mixed grids . Journal of Computational Physics, 2009, 228(21): 8161-8186.
Cockburn B, Shu C W. The local discontinuous Galerkin method for time-dependent convection-diffusion systems. SIAM Journal on Numerical Analysis, 1998, 35(6): 2440-2463.

## Slide 60: 参考文献（6）
Bassi F, Rebay S. A high-order accurate discontinuous finite element method for the numerical solution of the compressible Navier–Stokes equations. Journal of computational physics, 1997, 131(2): 267-279.
Gottlieb S, Shu C W, Tadmor E. Strong stability-preserving high-order time discretization methods. SIAM review, 2001, 43(1): 89-112.
Smagorinsky J. General circulation experiments with the primitive equations: I. The basic experiment. Monthly weather review, 1963, 91(3): 99-164.
Germano M, Piomelli U, Moin P, et al. A dynamic subgrid‐scale eddy viscosity model. Physics of Fluids A: Fluid Dynamics, 1991, 3(7): 1760-1765.
Meneveau C, Lund T S, Cabot W H. A Lagrangian dynamic subgrid-scale model of turbulence. Journal of Fluid Mechanics, 1996, 319: 353-385.
Meneveau C, Katz J. Scale-invariance and turbulence models for large-eddy simulation. Annual Review of Fluid Mechanics, 2000, 32(1): 1-32.
Zang Y, Street R L, Koseff J R. A dynamic mixed subgrid‐scale model and its application to turbulent recirculating flows. Physics of Fluids A: Fluid Dynamics, 1993, 5(12): 3186-3196.

## Slide 61: 参考文献（7）
Grinstein F F, Margolin L G, Rider W J (Eds). Implicit large eddy simulation: computing turbulent fluid dynamic]. Cambridge: Cambridge university press, 2007.
Li Y, Wang Z J. A priori and a posteriori evaluations of sub-grid scale models for the Burgers’ equation. Computers & Fluids, 2016, 139: 92-104.
Domaradzki J A, Xiao Z, Smolarkiewicz P K. Effective eddy viscosities in implicit large eddy simulations of turbulent flows. Physics of Fluids, 2003, 15(12): 3890-3893.
Roshko A. Experiments on the flow past a circular cylinder at very high Reynolds number. Journal of Fluid Mechanics, 1961, 10(03): 345-356.
Kravchenko A G, Moin P. Numerical studies of flow over a circular cylinder at Re D= 3900. Physics of fluids, 2000, 12(2): 403-417.
Geuzaine C, Remacle J F. Gmsh: A 3-D finite element mesh generator with built-in pre-and post-processing facilities. International Journal for Numerical Methods in Engineering, 2009, 79(11): 1309-1331.
Norberg C. An experimental investigation of the flow around a circular cylinder: influence of aspect ratio. Journal of Fluid Mechanics, 1994, 258: 287-316.

## Slide 62: 参考文献（8）
Lehmkuhl O, Rodríguez I, Borrell R, et al. Low-frequency unsteadiness in the vortex formation region of a circular cylinder. Physics of Fluids, 2013, 25(8): 85-109.
Lourenco L M, Shih C. Characteristics of the plane turbulent near wake of a circular cylinder, a particle image velocimetry study. Private communication, 1993.
Ong L, Wallace J. The velocity field of the turbulent very near wake of a circular cylinder. Experiments in fluids, 1996, 20(6): 441-453.
Mittal R, Moin P. Suitability of upwind-biased finite difference schemes for large-eddy simulation of turbulent flows. AIAA journal, 1997, 35(8): 1415-1417.
Duprat C, Balarac G, Métais O, Congedo, P. M, Brugière, O. A wall-layer model for large-eddy simulations of turbulent flows with/out pressure gradient. Physics of Fluids, 2011, 23(1): 015101.
Lodato G, Castonguay P, Jameson A. Structural wall-modeled LES using a high-order spectral difference scheme for unstructured meshes. Flow, turbulence and combustion, 2014, 92(1-2): 579-606.

## Slide 63: 参考文献（9）
Park G I, Moin P. An improved dynamic non-equilibrium wall-model for large eddy simulation. Physics of Fluids, 2014, 26(1): 37-48.
Kalitzin G, Medic G, Iaccarino G, Durbin P. Near-wall behavior of RANS turbulence models and implications for wall functions[J]. Journal of Computational Physics, 2005, 204(1): 265-291.
Coles D. The law of the wake in the turbulent boundary layer[J]. Journal of Fluid Mechanics, 1956, 1(02): 191-226.
Berger M, Aftosmis M. Progress towards a Cartesian cut-cell method for viscous compressible flow. //50th AIAA Aerospace Sciences Meeting Including the New Horizons Forum and Aerospace Exposition. 2012: 1301.
Ridders C. A new algorithm for computing a single root of a real continuous function. IEEE Transactions on circuits and systems, 1979, 26(11): 979-980.
Dean R B. Reynolds number dependence of skin friction and other bulk flow variables in two-dimensional rectangular duct flow. J. Fluids Eng, 1978, 100(2): 215-223.
Nikitin N V, Nicoud F, Wasistho B, Squires K D, Spalart P R. An approach to wall modeling in large-eddy simulations. Physics of fluids, 2000, 12(7): 1629-1632.

## Slide 64: 参考文献（10）
Fröhlich J, Mellen C P, Rodi W, Temmerman L, Leschziner M A, Highly resolved large-eddy simulation of separated flow in a channel with streamwise periodic constrictions. Journal of Fluid Mechanics, 2005, 526: 19-66.
Rapp C, Manhart M. Flow over periodic hills: an experimental study. Experiments in fluids, 2011, 51(1): 247-269.
Sherry M, Jacono D L, Sheridan J. An experimental investigation of the recirculation zone formed downstream of a forward facing step. Journal of Wind Engineering and Industrial Aerodynamics, 2010, 98(12): 888-894.
Zukoski E E. Turbulent boundary-layer separation in front of a forward-facing step. AIAA journal, 1967, 5(10): 1746-1753.
Largeau J F, Moriniere V. Wall pressure fluctuations and topology in separated flows over a forward-facing step. Experiments in Fluids, 2007, 42(1): 21.
Camussi R, Felli M, Pereira F, et al. Statistical properties of wall pressure fluctuations over a forward-facing step. Physics of Fluids, 2008, 20(7): 075113.
Oztop H F, Mushatet K S, Yılmaz İ. Analysis of turbulent flow and heat transfer over a double forward facing step with obstacles. International Communications in Heat and Mass Transfer, 2012, 39(9): 1395-1403.

## Slide 65: 参考文献（11）
Chiba K, Ishida R, Nakamura K. Mechanism for entry flow instability through a forward-facing step channel. Journal of non-newtonian fluid mechanics, 1995, 57(2-3): 271-282.
Stüer H, Gyr A, Kinzelbach W. Laminar separation on a forward facing step. European Journal of Mechanics-B/Fluids, 1999, 18(4): 675-692.
Baron A, Tsou F K, Aung W. Flow field and heat transfer associated with laminar flow over a forward-facing step. //The 8th International Heat Transfer Conference, San Francisco. 1986: 22-29.
Wilhelm D, Hartel C, Kleiser L. Computational analysis of the two-dimensional-three-dimensional transition in forward-facing step flow. Journal of Fluid Mechanics, 2003, 489(1-27): 168.
Edelmann C A. Influence of forward-facing steps on laminar-turbulent transition. Ph. D. Dissertation, University of Stuttgart, 2014.
Schlichting H, Gersten K, Krause E, Oertel H. Boundary-layer theory. New York: McGraw-hill, 1960.

## Slide 66: 参考文献（12）
Menter F R, Langtry R B, Likki S R, Suzen Y B, Huang P G, Völker S. A correlation-based transition model using local variables—Part I: model formulation[J]. Journal of turbomachinery, 2006, 128(3): 413-422.
Wang L, Fu S. Development of an intermittency equation for the modeling of the supersonic/hypersonic boundary layer flow transition. Flow, turbulence and combustion, 2011, 87(1): 165-187.