## Slide 1: 基于通量重构方法的 高精度湍流模拟研究
博士研究生：朱辉
指导教师：符松 教授
2017.5

## Slide 2: 目录
绪论
通量重构方法
高精度隐式大涡模拟研究
前台阶转捩流动研究
结论与展望

## Slide 3: 1.绪论

## Slide 4: 从“LAST”谈起
Laboratory for Advanced Simulation of Turbulence
传统湍流模拟
  传统湍流模拟方法：RANS
  传统数值方法：二阶有限体积法/ 多块结构网格
先进湍流模拟
  精细湍流模拟方法：DES/ LES/ DNS
  新型数值方法：高分辨率格式/ 高精度方法/ 非结构网格

## Slide 5: 高精度数值方法
实现高精度的关键
  单元内多项式分布
  通量/守恒量积分点
一般原则：
  精度=多项式次数+1
  积分精度与求解精度匹配
多项式表达
  基函数+DOF
  Modal：正交多项式基，DOF物理意义不明确
  Nodal：Lagrange多项式基，DOF就是节点的值

## Slide 6: 高精度方法湍流模拟（1）
雷诺平均（RANS）& 脱体涡模拟（DES）
  数值刚性
实现技巧
  “一维线搜索”
  自适应网格
  人工粘性/限制器
Gao J, Li X. Numerical Simulation of the Noise from Tandem Cylinder Flow with Spectral Difference Method
Shi L, Zhou C, Wang Z J. Adaptive RANS Solution with the High-order Correction Procedure via Reconstruction Method
Notes: 北航李晓东DES
周成2D SA

## Slide 7: 高精度方法湍流模拟（2）
直接数值模拟（DNS）
  简单外形
  低雷诺数
  高精度有限差分
大涡模拟
  壁面处理
  高精度方法的数值优势？
Li XL, Fu DX, Ma YW. Direct numerical simulation of a spatially evolving supersonic turbulent boundary layer at Ma= 6
Vermeire B C, Nadarajah S, Tucker P G. Canonical test cases for high-order unstructured implicit large eddy simulation
Notes: 李新亮，高超声速DNS
Paul Tucker, 高阶LES

## Slide 8: 研究目标
基于高精度通量重构的大涡模拟
  隐式大涡模拟
基于高精度隐式大涡模拟的壁面模型
  如何克服数值刚性问题？
  如何避免对数区偏差？
高精度通量重构方法在流动转捩问题上的应用
  前台阶转捩流动

## Slide 9: 2.通量重构方法

## Slide 10: 通量重构方法（FR/CPR）
Flux Reconstruction
  也称为Correction Procedure via Reconstruction
Huynh 2007
节点型有限单元法 (Nodal FEM)
  单元内多自由度
  无显式数值积分
统一框架
  不同的修正系数对应了不同的高阶方法

## Slide 11: 通量重构方法（FR/CPR）
Solution Points & Flux Points
重构
  利用Solution Points上的值重构出多项式分布
单元界面：
  类似FVM，用Riemann Solver算连续通量
修正
  利用单元界面的连续通量修正多项式

## Slide 12: 数学形式
最终形式：在每个单元内
微分形式，避免了数值积分，比DG省计算量
每个单元仅受到相邻单元影响，数值格式是紧致的，边界条件实施较简单，容易并行化

## Slide 13: 粘性项的计算: BR2格式
简单处理 = “危险的”非物理解
  本单元梯度也需要修正过程，否则不守恒
  边界处梯度不能直接平均！(Cockburn & Shu 1998)
尽可能紧致！
Bassi-Rebay 2格式
  Bassi & Rebay (2000), for DG
  Huynh (2009): “翻译”到CPR框架下

## Slide 14: 计算程序MUSIC
多物理场模拟程序
  Multiphysics Simulation Code
  基于通量重构方法
  原始版本由ZJ Wang教授课题组开发
现代化程序
  采用C++编写，使用Petsc等第三方库
  预留多物理场求解接口
并行计算
  MPI，支持大规模并行（目前最多使用2000进程并行）
新型数值方法
  hp adaptation

## Slide 15: 测试算例
Theoretical Order | Grid Size | L2 Error | Actual Order
2 | 10*10 | 3.060e-2 | -
 | 20*20 | 7.295e-3 | 2.07
 | 40*40 | 1.933e-3 | 1.99
3 | 10*10 | 7.406e-3 | -
 | 20*20 | 1.032e-3 | 2.84
 | 40*40 | 1.385e-4 | 2.87
4 | 10*10 | 1.358e-3 | -
 | 20*20 | 1.028e-4 | 3.72
 | 40*40 | 7.330e-6 | 3.77

## Slide 16: 3.高精度隐式大涡模拟研究

## Slide 17: Large Eddy Simulation
基本思想&原理
  “过滤”
  解析大尺度，模化小尺度
  存在普适的频谱性质
  可能存在普适的模型
常见模型
  Static Smagorinsky
  Dynamic Smagorinsky
  Scale Similarity
  Mixing Model = Smagorinsky + Scale Similarity
  Implicit LES

## Slide 18: Smagorinsky模型的缺陷
基于混合长假设
  缺乏物理基础
纯耗散性
“可实现性”
壁面极限SGS应力不等于零
对于高阶格式，Implicit LES可能优于Smagorinsky
  Li and Wang 2015
隐式大涡模拟具有潜力
Li Y, Wang Z J. A priori and a posteriori evaluations of sub-grid scale models for the Burgers’ equation
Notes: 可实现性:亚格子k>0，实际上有更严格的要求

## Slide 19: 基于通量重构的隐式大涡模拟
以三阶通量重构方法为例（定性分析）
  由格式线性分析得出
  假设网格尺度处于惯性子区
  小于网格尺度时，等效粘性系数随波数增加升高
Domaradzki J A, Xiao Z, Smolarkiewicz P K. Effective eddy viscosities
in implicit large eddy simulations of turbulent flows

## Slide 20: Cylinder at ReD=3900 (1)
亚临界雷诺数
  层流边界层+湍流尾迹
P3曲边网格
  53,910单元数
  展向15层
三阶/四阶通量重构
隐式大涡模拟
初始条件：
  均匀场 + 非对称光滑扰动

## Slide 21: Cylinder at ReD=3900 (2)
壁面压力分布
  三阶、四阶均与实验符合良好

## Slide 22: Cylinder at ReD=3900 (3)

## Slide 23: RANS vs LES
RANS
  网格需求低
  可以做二维/定常计算
  对分离流动模拟能力较弱
  用于高阶方法时存在数值困难
LES
  网格需求较高
  三维，非定常
  壁面附近的“大涡”尺度很小，大部分网格集中在此区域

## Slide 24: Detached Eddy Simulation
Spalart 1997, RANS -> LES
改进版本
  Delayed DES (DDES): 消除了网格诱导分离
  Improved DDES (IDDES): 消除了Log-Layer-Mismatch
依然存在的问题
  “灰区”
A Comprehensive Study of Detached Eddy Simulation, Mockett 2009

## Slide 25: Wall Modelled LES
降低壁面附近的网格量需求
三种常见策略
  改变边界条件：用切应力边界代替无滑移边界 (不稳定)
  嵌套网格：在壁面附近求解RANS方程 (复杂)
  涡粘模式：在壁面附近引入RANS涡粘系数 (✔）

## Slide 26: 新型壁面模型设计目标
不求解湍流模式方程
  数值刚性
远离壁面区域变为隐式大涡模拟
降低壁面附近流向&展向网格需求
  法向网格仍要求较密，以保持数值稳定
尽可能只使用“当地变量”
避免对数区不匹配

## Slide 27: S-A模式的近壁代数近似
Durbin 2004
粘性底层
  fv1分母趋于常数
  fv1整体正比于y+的三次方
  涡粘系数正比于y+的四次方
对数区
  fv1整体趋于1
  涡粘系数正比于y+

## Slide 28: Y+的计算
湍流边界层尺度定义
等应力层假设（零压梯度）
代入上述代数涡粘模式，积分此方程

## Slide 29: 新型壁面模型计算过程
在壁面第一层网格内
  取采样点计算
  目前取离壁面最远的求解点
根据u+和y+关系式求解y+
  Ridder’s算法，5到10步即可收敛
将y+插值到第一层网格内所有的求解点和通量点
  网格类型已知，求解点和通量点位置已知
  若对涡粘系数直接插值，易产生数值不稳定
判断最大y+
  若大于30，计算完成；否则在法向下一层网格中继续计算

## Slide 30: 槽道湍流(1)
三个不同雷诺数
  Reτ= 395, 640, 1140
不同网格
  流向、展向不同网格密度&法向网格分布
算例 | 名义Reτ | Nx×Ny×Nz | 第一层网格y+ | 第一个求解点y+ | 使用壁面模型
Case1 | 640 | 16×24×16 | 12 | 0.833 | 否
Case2 | 640 | 32×24×32 | 12 | 0.833 | 否
Case3 | 395 | 16×24×16 | 12 | 0.833 | 是
Case4 | 640 | 16×24×16 | 12 | 0.833 | 是
Case5 | 1140 | 16×24×16 | 12 | 0.833 | 是
Case6 | 640 | 16×24×16 | 8 | 0.556 | 是
Case7 | 640 | 32×24×32 | 12 | 0.833 | 是

## Slide 31: 槽道湍流(2)
如果不使用壁面模型：case 1, 2
  稀网格x+=50：速度型偏差，摩阻系数偏低20%
  加密到x+=25：稍有改善，但摩阻系数仍偏低10%

## Slide 32: 槽道湍流(3)
不同雷诺数：case 3,4,5
  Reτ=395, 640, 1140，
  均符合对数律分布
网格敏感性验证：case4,6,7
  法向网格分布：y+=8~12
  流向/展向加密
  基本上网格无关

## Slide 33: 槽道湍流(4)
壁面模型的转换区
  雷诺应力尖点对应于buffer layer速度拐折
  对其他区域几乎没有影响

## Slide 34: 周期山算例(1)
顺压/逆压梯度
  超出壁面模型设计范围
Reb = 2800, 10595
  低雷诺数：LES常见算例
  高雷诺数：ATAAC算例
网格：
  P3曲边网格
  Nx×Ny×Nz
  = 32×32×16
  高雷诺数下对应ATAAC稀网格

## Slide 35: 周期山算例(2)
无壁面模型
  再附点提前
有壁面模型
  再附点与参考值接近

## Slide 36: 周期山算例(3)
速度型

## Slide 37: 4.前台阶转捩流动研究

## Slide 38: 前台阶流动
二维几何扰动
  是否会引起转捩？
流动物理比后台阶更复杂
  两个分离区
基本参数
  台阶高度与边界层高度之比 （小于1）
  基于台阶高度的雷诺数 （处于转捩区间）
适用隐式大涡模拟
  显式LES难以计算转捩SGS应力
  DNS计算量难以承受

## Slide 39: 文献(1)
以雷诺数分类
  很低，关注小扰动的发展
    Wilhelm et. al. 2003 (JFM)：二维扰动如何变成三维扰动
  很高，关注湍流边界层
    Zukoski 1967 (AIAA J)：台阶前的第一分离区，超声速
    Sherry et. al. 2010：台阶后的第二分离区

## Slide 40: 文献(2)
转捩雷诺数
  Edelmann 2014 (DLR)
    台阶上游壁面吹吸与波包演化
    Reh = 400~4440
    扰动方程DNS
    线性稳定性分析
Edelmann C A. Influence of forward-facing steps on laminar-turbulent transition

## Slide 41: 问题与算例
台阶与入口扰动如何相互作用？（中等雷诺数）
Reh=720, Rexin=186624, Rexstep=330624
层流入口 + 有限扰动
  低频三维扰动，类似T-S波
四阶通量重构
DOF ≈ 1500万
展向宽度30h
展向32单元
统计50万时间步

## Slide 42: 平均流动(1)
速度型
与平板对比
  同样的入口扰动下，平板不转捩

## Slide 43: 平均流动(2)
湍动能
  在台阶前开始产生
估算涡粘系数
  <u’v’> = μt×dU/dy

## Slide 44: 5.总结与展望

## Slide 45: 总结与展望
基于通量重构方法的隐式大涡模拟
  验证其性能
适用于隐式大涡模拟的新型壁面模型
  代数形式
  不求解湍流模型方程
  仅使用当地变量
  优化模型参数？
前台阶诱导转捩流动
  转捩机理
  不同雷诺数/台阶高度研究？

## Slide 46: 已发表的学术成果
[1] Hui Zhu, Song Fu, Lei Shi, and Z. J. Wang, "Implicit Large-Eddy Simulation for the High-Order Flux Reconstruction Method", AIAA Journal, Vol. 54, No. 9, (2016), pp. 2721-2733.
[2] Hui Zhu, Song Fu, "Forward Facing Step Roughness Effect on Hypersonic Boundary Layer Flow", APCOM 2014
[3] 朱辉，肖志祥，符松，某先进战斗机大攻角气动性能及其控制研究，国防技术报告, 2012
[4] Hui Zhu, Song Fu, Lei Shi, and Z. J. Wang, " A Hybrid RANS-Implicit LES Approach for the High-Order FR/CPR Method ", 54th AIAA Aerospace Sciences Meeting, 2016

## Slide 47: 参考文献(1)
[1] Wang Z J. Adaptive high-order methods in computational fluid dynamics[M]. World Scientific, 2011.
[2] Cockburn B, Shu C W. TVB Runge-Kutta local projection discontinuous Galerkin finite element method for conservation laws. II. General framework[J]. Mathematics of computation, 1989, 52(186): 411-435.
[3] Liu Y, Vinokur M, Wang Z J. Multi-dimensional spectral difference method for unstructured grids[C], 43rd AIAA Aerospace Sciences Meeting and Exhibit. 2005: 320.
[4] Li W, Ren Y X. High‐order k‐exact WENO finite volume schemes for solving gas dynamic Euler equations on unstructured grids[J]. International Journal for Numerical Methods in Fluids, 2012, 70(6): 742-763.
[5] Gottlieb S, Shu C W, Tadmor E. Strong stability-preserving high-order time discretization methods[J]. SIAM review, 2001, 43(1): 89-112.

## Slide 48: 参考文献(2)
[6] Gao J, Li X. Numerical Simulation of the Noise from Tandem Cylinder Flow with Spectral Difference Method[C], 54th AIAA Aerospace Sciences Meeting. 2016: 0256.
[7] Shi L, Zhou C, Wang Z J. Adaptive RANS Solution with the High-order Correction Procedure via Reconstruction Method[C], 54th AIAA Aerospace Sciences Meeting. 2016: 1826.
[8] Li XL, Fu DX, Ma YW. Direct numerical simulation of a spatially evolving supersonic turbulent boundary layer at Ma= 6[J]. Chinese Physics Letters, 2006, 23(6): 1519.
[9] Vermeire B C, Nadarajah S, Tucker P G. Canonical test cases for high-order unstructured implicit large eddy simulation[C], 52nd Aerospace Sciences Meeting. 2014: 0935.
[10] Li Y, Wang Z J. A priori and a posteriori evaluations of sub-grid scale models for the Burgers’ equation[J]. Computers & Fluids, 2016, 139: 92-104.

## Slide 49: 参考文献(3)
[11] Vreman B, Geurts B, Kuerten H. Realizability conditions for the turbulent stress tensor in large-eddy simulation[J]. Journal of Fluid Mechanics, 1994, 278: 351-362.
[12] Norberg C. An experimental investigation of the flow around a circular cylinder: influence of aspect ratio[J]. Journal of Fluid Mechanics, 1994, 258: 287-316.
[13] Kravchenko A G, Moin P. Numerical studies of flow over a circular cylinder at Re D= 3900[J]. Physics of fluids, 2000, 12(2): 403-417.
[14] Mittal R, Moin P. Suitability of upwind-biased finite difference schemes for large-eddy simulation of turbulent flows[J]. AIAA journal, 1997, 35(8): 1415-1417.
[15] Berger M, Aftosmis M. Progress towards a Cartesian cut-cell method for viscous compressible flow[C]//50th AIAA Aerospace Sciences Meeting Including the New Horizons Forum and Aerospace Exposition. 2012: 1301.

## Slide 50: 参考文献(4)
[16] Shur M L, Spalart P R, Strelets M K, et al. A hybrid RANS-LES approach with delayed-DES and wall-modelled LES capabilities[J]. International Journal of Heat and Fluid Flow, 2008, 29(6): 1638-1649.
[17] Lodato G, Castonguay P, Jameson A. Structural wall-modeled LES using a high-order spectral difference scheme for unstructured meshes[J]. Flow, turbulence and combustion, 2014, 92(1-2): 579-606.
[18] Kalitzin G, Medic G, Iaccarino G, et al. Near-wall behavior of RANS turbulence models and implications for wall functions[J]. Journal of Computational Physics, 2005, 204(1): 265-291.
[19] Edelmann C A. Influence of forward-facing steps on laminar-turbulent transition[D]. University of Stuttgart, 2014.
[20] Stüer H, Gyr A, Kinzelbach W. Laminar separation on a forward facing step[J]. European Journal of Mechanics-B/Fluids, 1999, 18(4): 675-692.

## Slide 51: 参考文献(5)
[21] Wilhelm D, Hartel C, Kleiser L. Computational analysis of the two-dimensional-three-dimensional transition in forward-facing step flow[J]. Journal of Fluid Mechanics, 2003, 489(1-27): 168.
[22] Zukoski E E. Turbulent boundary-layer separation in front of a forward-facing step[J]. AIAA journal, 1967, 5(10): 1746-1753.
[23] Sherry M, Jacono D L, Sheridan J. An experimental investigation of the recirculation zone formed downstream of a forward facing step[J]. Journal of Wind Engineering and Industrial Aerodynamics, 2010, 98(12): 888-894.
[24] Domaradzki J A, Xiao Z, Smolarkiewicz P K. Effective eddy viscosities in implicit large eddy simulations of turbulent flows[J]. Physics of Fluids, 2003, 15(12): 3890-3893.